## Slide 1: River Guardian Western Streams Update Water Quality Monitoring Sam Frith

## Slide 2: Thank You!
Without your volunteered time and energy, we would not have as good an idea of the health of the Western Streams as we do.
As a guardian, you know your river and can quickly report when something changes, red flagging an incident or a pollution source

## Slide 5: Western Stream Operational Catchment
Western Streams Operational Catchment Data Explorer

## Slide 6: Data Overview
243 River guardian surveys have been submitted
60 Different sites have been monitored
At least 29 of these have been monitored 4 times
Jan 1st -
July 15th
2026

## Slide 7: Phosphates Sites: Jan 2025 to July 2026

## Slide 8: Nitrates Sites: Jan 2025 to July 2026

## Slide 9: Result Ranges
Phosphate*1
Nitrate*2

## Slide 10: Result Ranges – Temperature and Turbidity
Temperatures
Turbidity

## Slide 11: Result Ranges – TDS
Rother results ranged from 26 to 900
All normal, but please do check measuring TDS and not F

## Slide 12: Ems
Ems | Catchment Data Explorer
Length: 8.8 km
Catchment Area: 60.1 km2
10 sites historically monitored to classify. 2 sites in 2022, Cycle 3
Brook Meadow - Invertebrates
Mill Pond – Ammonia, Dissolved Oxygen, Phosphate, Temp
Reason for Not Achieving Good (RNAG)
Flow, from Abstraction, impacts:
Invertebrates
Fish
Hydrological Regime
Physical Modifications, Flood protection, impacts:
Invertebrates
Fish
Other reasons:
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)
Water Framework Directive (WFD)

## Slide 13: Ems – Result Averages Jan 2026 to July 2026
Moderate
Poor

## Slide 14: Hambrook – Result Averages Jan 2026 to July 2026
Moderate
Poor
No EA Data for WFD status
Water Framework Directive

## Slide 15: Bosham
Bosham Stream | Catchment Data Explorer
Length: 3.8 km
Catchment Area: 21.9 km2
5 sites historically monitored to classify.
1 site in 2022, Cycle 3
Colner Creek – Ammonia, Dissolved Oxygen, Phosphate, Temp
Reason for Not Achieving Good (RNAG)
Flow, from Abstraction, impacts:
Hydrological Regime
Physical Modifications, Urban & Transport, impacts:
Fish
Other reasons:
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)

## Slide 16: Bosham – Result Averages Jan 2026 to July 2026
Moderate
Poor

## Slide 17: Broad Rife
Broad Rife | Catchment Data Explorer
Length: 2.9 km
Catchment Area: 27.9 km2
5 sites historically monitored to classify. 2 sites in 2022, Cycle 3
Ferry Pool Pond sluice and Sidlesham WWTW
Ammonia, Dissolved Oxygen, Phosphate, Temp
Reason for Not Achieving Good (RNAG):
Sewage (continuous)
Physical Modifications from Agriculture & Rural Land Management, Land Drainage & Poor soil management
Saline Intrusion
Impacts:
Invertebrates, Ammonia, Phosphate, Dissolved Oxygen
Reasons ‘Unknown’ - Under/Pending Investigation:
Benzo(ghi)perylene (occurs naturally in crude oil and coal tar)
Perfluorooctane sulphonate (PFOS)
Awaiting recovery from delivered measures
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)
Sidlesham WWTW currently unmonitored by RG (Keynor Rife in march 2025)

## Slide 18: Broad Rife
Broad Rife | Catchment Data Explorer
West Wittering Rife
Almodington Rife
Highleigh Rife

## Slide 19: Broad Rife – Result Averages Jan 2026 to July 2026
Moderate
Poor

## Slide 20: Bremere Rife
Bremere Rife | Catchment Data Explorer
Length: 4 km
Catchment Area: 11.3 km2
3 sites historically monitored to classify.
0 sites monitored in 2022, Cycle 3:
Last was 2019 was:
South of Fisher – Macrophytes
Halsey Farm – Ammonia, DO, Phosphate, Temp
Reason for Not Achieving Good (RNAG):
Agriculture - Poor Soil & Nutrient Management
Drought - Flow
Impacts:
Invertebrate, Ammonia, Phosphate, Dissolved oxygen
Awaiting recovery from delivered measures:
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)

## Slide 21: Bremer Rife – Result Averages Jan 2026 to July 2026
Moderate
Poor

## Slide 22: Lavant
Lavant (Sussex) | Catchment Data Explorer
Length: 15.4 km
Catchment Area: 91.1 km2
7 sites historically monitored to classify.
1 site in 2022, Cycle 3:
Apuldram – Ammonia, Dissolved Oxygen, Phosphate, Temp
Reason for Not Achieving Good (RNAG)
Sewage (continuous)
Impacts - Fish, Phosphate, Invertebrates
Other reasons:
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)
Macrophytes and Phytobenthos (plants and algae)

## Slide 23: Lavant – Result Averages Jan 2026 to July 2026
Moderate
Poor
Dry Sites:
Tozer Way - January and July
Chichester College, west branch - due to ongoing construction work!

## Slide 24: Pagham Rife
Pagham Rife | Catchment Data Explorer
Length: 10.3 km
Catchment Area: 33.4 km2
8 sites historically monitored to classify.
1 site in 2022, Cycle 3:
By The Salt House – Ammonia, Temp, Dissolved Oxygen (Bad), Phosphate, Acid Neutralising Capacity
Reason for Not Achieving Good (RNAG):
Sewage (continuous)
Physical Modifications - Flood Protection, Reservoir, Land Drainage
Agricultural – Poor Soil Management, Poor Nutrient Management
Invasive (floating Pennywort)
Impacts:
Flow, Temp, Fish, Invertebrates, Ammonia, Phosphate, Dissolved Oxygen, Macrophytes and Phytobenthos (plants and algae),
Reasons ‘Unknown’ - Under/Pending Investigation:
Perfluorooctane sulphonate (PFOS)
Awaiting recovery from delivered measures
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)

## Slide 25: Pagham Rife – Result Averages Jan 2026 to July 2026
Moderate
Poor
Data including:
RLFAS = River Lavant Flood Alleviation Scheme
Also known as Chichester Flood Relief Channel

## Slide 26: Aldingbourne Rife
Aldingbourne Rife | Catchment Data Explorer
Length: 10.3 km
Catchment Area: 51.2 km2
7 sites historically monitored to classify.
3 sites in 2022, Cycle 3:
Bognor - Upstream Bultins, Tesco, U/S Gladius Way
All monitored - Ammonia, Dissolved Oxygen (DO), Phosphate, Temp
Reason for Not Achieving Good (RNAG):
Misconnections, Road Run-off, Sewage (continuous), Poor Soil Management, Poor Nutrient Management, Land Drainage, Flood Protection
Impacts:
Invertebrates, Phosphate, DO, Fish,
Awaiting recovery from delivered measures
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)

## Slide 27: Lidsey Rife
Lidsey Rife | Catchment Data Explorer
Length: 6.35 km
Catchment Area: 35.6 km2
6 sites historically monitored to classify.
1 site in 2022, Cycle 3:
Bognor – Behind Sainsbury before joining Aldingbourne
Monitored - Ammonia, Dissolved Oxygen (Bad), Phosphate, Temp
Reason for Not Achieving Good (RNAG):
Misconnections, Sewage (continuous), Drought, Poor Soil Management, Horticulture
Impacts:
Invertebrates, Phosphate, Dissolved Oxygen
Awaiting recovery from delivered measures
Mercury and its Compounds
Polybrominated diphenyl ethers (PBDE)(flame‑retardant chemicals)

## Slide 28: Aldingbourne & Lidsey – Result Averages Jan 2026 to July 2026
Moderate
Poor

## Slide 29: Rainfall Data at Fishbourne – last 6 months
Hydrology Data Explorer - Fishbourne

## Slide 30: Groundwater Data at Chilgrove – last 6 months
Hydrology Data Explorer - Chilgrove House
Meters above ordnance datum

## Slide 31: Flow Data at Graylingwell – last 6 months
Hydrology Data Explorer - Graylingwell

## Slide 32: Water Level Data at Graylingwell – last 6 months
Hydrology Data Explorer - Graylingwell

## Slide 33: Any Questions??

## Slide 34: Riverfly review
12 sites have been monitored by
WSRT and Friends of the Ems groups
61 surveys completed
4 sites on the Ems
2 sites on the Ham Brook,
2 sites on the Bosham
4 sites on the Lavant
1st January 2026 to 16th July 2026

## Slide 35: Riverfly Locations

## Slide 36: Riverfly review - Ems
Species Found:
Cased Caddis
Caselesss Caddis
Blue-Winged Olive
Olives (Baetidae)
Stoneflies
Freshwater Shrimp
No:
Mayfly (Ephemeridae)
Flat-Bodied Stone Clinger
4 sites monitored:
Walderton Junction
Brooklyn Cottage
Mill Meadows Farm (Trigger of 7)
Brook Meadows (Trigger of 7)
Walderton reported Low/No flow in June
Brook Meadows flooded in Feb
Highest RMI score was 14 at
Brooklyn Cottage
Lowest score was 2 at Walderton Junction

## Slide 37: Riverfly review - Hambrook
Species Found:
Cased Caddis
Caselesss Caddis
Blue-Winged Olive
Olives (Baetidae)
Freshwater Shrimp
No:
Mayfly (Ephemeridae)
Flat-Bodied Stone Clinger
2 sites monitored:
Blackbarn (Trigger of 7)
School Lane (Trigger of 5)
Highest RMI score was 12 at School Lane
Lowest RMI scores were 9 at both site

## Slide 38: Riverfly review - Bosham
Species Found:
Cased Caddis
Caselesss Caddis
Blue-Winged Olive
Olives (Baetidae)
Stoneflies
Freshwater Shrimp
No:
Mayfly (Ephemeridae)
Flat-Bodied Stone Clinger
2 sites monitored:
Old Bridge Meadow (Trigger of 5)
The Millstream Hotel (Trigger of 5)
Highest RMI score was 12 at both sites
Lowest RMI scores was 5 at The Millsteam Hotel

## Slide 39: Riverfly review - Lavant
Species Found:
Cased Caddis
Caselesss Caddis
Blue-Winged Olive
Olives (Baetidae)
Stoneflies
Freshwater Shrimp
No:
Mayfly (Ephemeridae)
Flat-Bodied Stone Clinger
4 sites monitored:
Charlton
Marsh Lane
Sheepwash Lane (Trigger of 5)
Fordwater (Trigger of 5)

## Slide 40: Riverfly review - Lavant
Fordwater breached the trigger level, this is expected but not ideal.
Sheepwash Lane has now dried out for the summer (Winterbourne)
Highest RMI scores were 9 at Fordwater and Sheepwash
Lowest RMI scores was 0 at Marsh Lane and Sheepwash during first flow and first survey of the season in Jan

## Slide 41: Riverfly Results (Max)
Species | Count
Cased Caddis | Up to 1250
Caseless Caddis – | Up to 49
Mayfly (Ephemeridae) | None found in catchment
Blue-Winged Olive (Ephemerellidae) | Up to 1280
Flat-Bodied Stone Clinger (Heptageniidae) | None found in catchment
Olives (Baetidae) | Up to 450
Stoneflies (Plecoptera) | Up to 503
Freshwater Shrimp | Up to 1993

## Slide 42: Any Questions??

## Slide 45: Duplicate

## Slide 46
To move the pin
Open survey
Zoom in
Click on correct location

## Slide 47: Any Questions??

## Slide 48: Download Survey Data – 3 ways
1
For specific survey data, use the search box then click download

## Slide 49
2
Open the map, zoom in so that the pins you are interested in are shown on the map page.
Scroll down to the bottom of the legend and click
‘Download Map Data’
For multiple sites located close together

## Slide 50: 3
For larger areas

## Slide 51
Select the area you are interested in by clicking on the map

## Slide 53: Any Questions??

## Slide 54: Overview – Sewage Untreated
32 spilling assets in the Western Streams Catchment
Discharged untreated sewage 7870 times
for of over 16,367 hours
Spill data can be found and downloaded from:
Southern Water - Rivers and Seas Watch
Check EDM data and download via:
Event Duration Monitoring - Storm Overflow Explorer

## Slide 56
Spill hours rounded down from Rivers & Seas website data on 21st July 2026

## Slide 57: Sewage Discharges – RG Monitoring
15* sites are not currently being monitored regularly both up and downstream:
*This list has not been checked recently. If you are interested in taking on one of them then please chat with Sam.

## Slide 58: Other Issues
Soil run-off
Livestock poaching riverbanks
Farms
Golf courses, run off from fertilizers & abstraction
What else are you finding?

## Slide 59: Kit Maintenance
Cleaning and drying your kit at the end of your survey day is good practice.
Prolongs the life of your monitoring equipment
Prevents the spread of invasive species (INNS)
Prevents nutrient and chemical contamination between samples
Hanna Checker cuvettes, water collection device, syringe, Secchi tube
Rinse out with warm water and leave to air dry
TDS/Temp monitor pens
Soak the tips in lukewarm water for 5 mins then air dry before replacing cap

## Slide 60: Health and Safety - reminders
Always go out in pairs
Let someone know where you are heading and what time you expect to be back
Always wear gloves – Protect from water and reagents
River Guardian Risk Assessment is being updated
Link: Home and Dry - Water Safety Course - West Mercia Search and Rescue
Link: Tick awareness A5 leaflet for printing